## Slide 1: ELECTRONIC TOLL COLLECTION USING PIEZOELECTRIC AND RFID SENSORS
Y.NAGA.SAI SUMANTH (18497)
V.RAMABHADRAM SAI (17552)

## Slide 2: E-Tolls System-Knowledge
Four integral processing in Electronic Toll Collection (ETC) system.
Automation vehicle identification
Automatic vehicle classification
Transaction processing
Violation Enforcement
Reference :
“Electronic Toll Collection System”, http://en.wikipedia.org/wiki/Electronic_toll_collection
“Apex Committee Survey Report on Statistics of Electronic Toll Collection System”, http://www.nhai.org/doc/17feb12/etc_apexcomm_report_final_7oct.pdf

## Slide 3: Overview Of The System
acquisition
PC (Lab VIEW)
PIEZO ELECTRIC SESORS
RFID Reader
RFID tag
Arduino UNO
Vehicle classified
o/p
DC VOLTAGE
SENSORS

## Slide 4: Piezoelectric Sensors
A piezoelectric sensor is a device that uses the piezoelectric effect, to measure change in pressure, acceleration, strain or force by converting them to an electric charge.
DC voltage is proportional to the stress applied on the surface of sensor.
Reference : http://www.explainthatstuff.com/piezoelectricity.html

## Slide 5: Arduino UNO
Not every pin on a microcontroller has the ability to do analog to digital conversions. On the Arduino board, these pins have an ‘A’ in front of their label (A0 through A5) to indicate these pins can read analog voltages.
Reads the value from the specified analog pin. The Arduino board contains a 6 channel (8 channels on the Mini and Nano, 16 on the Mega), 10-bit analog to digital converter. This means that it will map input voltages between 0 and 5 volts into integer values between 0 and 1023. This yields a resolution between readings of: 5 volts / 1024 units or, .0049 volts (4.9 mV) per unit.
Reference: https://www.arduino.cc/en/Main/ArduinoBoardUno

## Slide 6: RFID Reader & UART Interface
RDM 125KHz card mini-module is designed for reading code from 125KHz card compatible read tags . It can be applied in office/home security, personal identification, access control etc..
Here we are capturing continuous data
Support external antenna
Maximum effective distance up to 50mm
UART TTL interface
Support EM4100 compatible read only or read/write tags
RFID READER
USB 2.0 to TTL Module
Reference:
http://wiki.seeedstudio.com/wiki/125Khz_RFID_module_-_UART#How_to_buy

## Slide 7: RFID TAGS
Every vehicle carries a RFID tag.
The RFID TAG contains the details about the owner of the vehicle.
The details are needed for transaction processing of the vehicle.
When the RFID tag comes near the active region of the reader, the tag is identified and the information is passed.
In this project we are using 125KHZ RFID key tags.
Reference:
http:http://www.engineersgarage.com/insight/how-rfid-tag-works?page=2

## Slide 8: Programming in LabVIEW
It is a visual programming language.
It is a system design platform and development environment
RFID can be interfaced with LabVIEW also using Visa terminals.
Loops, charts functions and other signal manipulation functions are available.
LabVIEW is a graphical programming language created by National Instruments

## Slide 9: LabVIEW Programs Are Called Virtual Instruments (VI’s)
Each VI has 2 Windows
Front Panel
User Interface (UI)
  Controls = Inputs
  Indicators = Outputs
Block Diagram
Graphical Code
  Data travels on wires from controls through functions to indicators
  Blocks execute by Dataflow

## Slide 10: LabVIEW
Block Diagram Window
Front Panel Window
Input
Terminals
Output
Terminal
Boolean
Control
temperature
Indicator
Reference:
http://engineering.sdsu.edu/~johnston/me295/modules/labview/tutorials_and_exercises/temperature_control_2.htm

## Slide 11: LabVIEW Interfacing For Arduino
In order to interface LabVIEW with Arduino we have to dump the LIFA Base code in Arduino.
We can download the LIFA Base from NATIONAL INSTRUMENTS website.
We can dump LIFA Base code in Arduino board using Arduino software.
Reference: http:https://decibel.ni.com/content/docs/DOC-30365

## Slide 12: Hardware Interfacing
4
2
1
3
A0
A1
A2
A3
COM 3
COM 4
RFID tag
RFID Reader
USB UART
Arduino UNO Board
Piezoelectric Sensors
USB type B cable
buzzer
LEDS

## Slide 13: Axial Width Of Vehicles
Few popular Vehicles
Axle width lorry in centimetre
Ashok Leyland lorry -95.7
Tata lorry -84.252
Volvo Bus -93
Ashok Leyland Truck -95.6
Tata Motors 3118 Trucks -95.8
Reference : http://diyford.com/ford-axle-history-identification-ford-differentials/#

## Slide 14: Toll Rates For The Proposed System
BIKE TOLL - 10$
CAR TOLL - 20$
TRUCK TOLL - 30$
VIOLATION TOLL - 40$

## Slide 15: LabVIEW Program For The Proposed System

## Slide 16: Program Continued

## Slide 17: Program Continued

## Slide 18: Program Continued

## Slide 19: Program Continued

## Slide 24
When vehicle is classified the Yellow LED glows and if any Violation occurs the Red LED glows

## Slide 25
Piezoelectric Sensors alignment
RFID Reader and Cards

## Slide 26
Bike Toll message
Car Toll message
Truck Toll message
Violation Toll message

## Slide 27
THANK YOU